| SAFE WORK PRACTICE |
| --- |
| TITLE | Directional Drilling |
| GENERAL | Protecting workers from injuries associated with directional drilling operations |
| APPLICATION | The use of drilling equipment that can travel a directed path through the use of accurate tracking and guiding systems. That can be guided over, under and around utilities, structures, rivers and highways. |
| PROTECTIVE MECHANISMS | Safe work procedure Permit system Manufacturer specifications PPE Barricades and warning signs Surveyor Inspection ERP (Emergency Response Plan) |
| SELECTION AND USE | As per safe work procedure |
| SUPERVISOR RESPONSIBILITY | Supervisors are responsible to facilitate and/or provide proper instruction to their workers on protection requirements |
| WORKER RESPONSIBILITY | Barricades and warning signs in place. Ensure to expose utilities before boring. Ensure proper placement of mats, stakes and cones. Ensure grounding stakes are utilized. Test the strike alert system. Do not use pipe wrenches to uncouple drill rod. Do not modify any equipment. |
| * The information presented in this publication is intended for general use and may not apply to every circumstance. It is not a definitive guide to government regulations and does not relieve persons using this publication from their responsibilities under applicable legislation. The Northern Safety Association does not guarantee the accuracy of, nor assume liability for, the information presented here. Individual counselling and advice are available from the Association. |