| SAFE WORK PRACTICE |
| --- |
| TITLE | Purging Vessels and Piping Systems |
| GENERAL | Protecting workers from injuries associated with purging vessels and piping systems |
| APPLICATION | Vessels and related piping systems that have been in hydrocarbon service must be drained, vented and/or purged prior to “opening”. |
| PROTECTIVE MECHANISMS | Permit system Lockout and blinding procedure Safe work procedure PPE ERP (Emergency Response Plan) |
| SELECTION AND USE | As per safe work procedure Provincial OH&S Legislation |
| SUPERVISOR RESPONSIBILITY | Supervisors are responsible to facilitate and/or provide proper instruction to their workers on protection requirements and training. Work site inspections. Hazard Assessments. Ensure used inert material is disposed of according to legislation. |
| WORKER RESPONSIBILITY | Ensure system is isolated. Open drain and/or flare lines. Attach inert material source to vessel. Open vents. Ground system. Displace hazardous material with inert materials. Remove inert material and check for hazardous material leaks. Continually monitor work areas for changing conditions. Follow purging safe work procedure step by step. |
| * The information presented in this publication is intended for general use and may not apply to every circumstance. It is not a definitive guide to government regulations and does not relieve persons using this publication from their responsibilities under applicable legislation. The Northern Safety Association does not guarantee the accuracy of, nor assume liability for, the information presented here. Individual counselling and advice are available from the Association. |